## Slide 1
⚡ Aditya-L1 Flare Watch
Real-time solar-flare NOWCASTING from soft + hard X-rays
ISRO Hackathon · Problem Statement 15 · Minor Project — presented by Peeyush Raj
2,891
FLARES NOWCASTED
93.5%
DETECTION RATE
117 s
HARD-X PRECURSOR
21.2M
ROWS MERGED
Aditya-L1 Flare Watch · Minor Project · Solar-Flare Nowcasting
1

## Slide 2
THE PROBLEM & WHY IT MATTERS
Solar flares break technology. We need to see them live.
The threatFlares are sudden X-ray explosions on the Sun that can:• fry satellite electronics• black out GPS & radio for hours• collapse power grids (1989 Quebec)The opportunityAditya-L1, ISRO's solar observatory at the L1 point, watches the Sun 24×7 with two X-ray eyes — SoLEXS (soft) and HEL1OS (hard).PS-15 asks us to detect flares from BOTH instruments combined — in real time.
Nowcast vs ForecastNOWCAST — “a flare is happening RIGHT NOW”Detect + classify + alert within seconds of onset. THIS PROJECT (minor).FORECAST — “one is coming in the next 30 min”Predict before the peak. Prototype exists — deliberately reserved for the MAJOR project (next slide explains the split).PS-15 covers both; we deliver one half completely instead of two halves halfway.
Aditya-L1 Flare Watch · Minor Project · Solar-Flare Nowcasting
2

## Slide 3
SCOPE
Minor = nowcast. Major = forecast. One clean line.
MINOR — THIS PROJECT
MAJOR — FUTURE
Detect flares as they happen
✅ core
—
Soft+hard cross-matched catalog
✅ 2,891 flares
extends automatically
Counts → GOES class calibration
✅ validated
—
Merged single-file datasets
✅ 21.2M rows
—
Dashboard + live-alert replay
✅
—
Predict flares before peak
🔮 prototype only
✅ main deliverable
The forecast prototype is shown in the dashboard only as a clearly-marked FUTURE WORK panel.
Aditya-L1 Flare Watch · Minor Project · Solar-Flare Nowcasting
3

## Slide 4
DATA
From PRADAN zips to one clean table per second
What we downloaded (ISRO PRADAN)• SoLEXS: 203 daily zips — 2024-02-12, 2024-03-14→05-31, 2026-05-06→09-17• HEL1OS: 22 zips — 2026-09-07→09-18, 12-h segments, 4 detectors• Level-1 FITS: 1-second X-ray count rates + good-time intervals
Ground truth for validationNOAA GOES-16 XRS 1-min flux — the world's flare-class reference. 432 reference flares across 73 days; also used to calibrate our counts into physical flux.
📦 Merged dataset — the deliverable
solexs_merged
17.54M rows
179 MB pq / 1.39 GB csv
hel1os_merged
3.67M rows
32 MB pq / 263 MB csv
merged_all_data
21.2M rows
211 MB pq / 1.65 GB csv
master_catalog.csv
2,891 flares
classes, peaks, lead times
One row = one second: UTC time · rate · error · quality flag
Aditya-L1 Flare Watch · Minor Project · Solar-Flare Nowcasting
4

## Slide 5
METHOD — THE NOWCAST ENGINE
Hearing a shout above room noise — 5 steps
1
INGEST
FITS → 1-second tables; keep only good-time intervals
2
BACKGROUND
rolling 45-min MINIMUM — flares only push counts up, so the floor is immune
3
SMOOTH + 5σ
20-s average; flare when signal beats background by 5 standard deviations for 30 s
4
END & MERGE
decay below 1.5σ ends it; bursts within 300 s merge into one flare
5
CROSS-MATCH & CLASSIFY
link soft+hard views; counts → GOES flux → A/B/C/M/X
HEL1OS photon-starved 1-s samples are first re-binned to 60 s. Detector = backend/pipeline/detect/detector.py · 6/6 unit tests.
Aditya-L1 Flare Watch · Minor Project · Solar-Flare Nowcasting
5

## Slide 6
VALIDATION
93.5% of every real flare caught — validated against NOAA
93.5%
TRUE POSITIVE RATE
404/432 GOES reference flares detected
100%
X-CLASS CAUGHT
all 17 X-flares · M: 95.3% · C: 92.9%
4.7/day
FALSE ALARMS
…and they aren't even false — see below
The honest twist: our “false alarms” are real flares GOES never listedAll 345 unmatched detections are genuine C6–C8 solar events below GOES's detection floor (median significance 34σ). SoLEXS is MORE sensitive than the reference standard — the dashboard, docs and EVALUATION.md state this openly.
Aditya-L1 Flare Watch · Minor Project · Solar-Flare Nowcasting
6

## Slide 7
THE PHYSICS HIGHLIGHT
Hard X-rays arrive first — the Neupert effect, measured
Why two instruments?When a flare ignites:1. Electrons are slammed into the solar surface → HARD X-rays (HEL1OS) — first2. The blast-heated plasma then glows → SOFT X-rays (SoLEXS) — afterSo the hard-X peak is a built-in early warning of the soft-X peak — the Neupert effect, and the physical basis of forecasting.
Measured in our data:
117 s
median hard-before-soft lead (14 cross-matched events)
458 s longest observed lead
2026-09-07→09-15 overlap window, 59 flares
Aditya-L1 Flare Watch · Minor Project · Solar-Flare Nowcasting
7

## Slide 8
SOFTWARE & ARCHITECTURE
A reproducible pipeline, not a notebook
Stack• Python 3.11 · astropy · pandas · pyarrow• LightGBM (forecast prototype — future)• FastAPI + WebSocket live replay• React 19 + Vite + Recharts dashboardEngineering hygiene• 6/6 unit tests on synthetic light curves• deterministic CLI pipeline: ingest → detect → eval → export• 3.7 GB data kept out of git; rebuildable via export_merged.py• documented: README · DATASET · EXPLAINER · EVALUATION · RUN_GUIDE
What runs where
backend/pipeline/
ingest · detect · catalog · eval · export_merged
backend/app/
FastAPI: 6 REST endpoints + WS replay
frontend/
dashboard + guide/glossary page
backend/data/merged/
the merged dataset deliverable
docs (5 .md)
methods, metrics, demo script, glossary
Aditya-L1 Flare Watch · Minor Project · Solar-Flare Nowcasting
8

## Slide 9
LIVE DEMO
The dashboard — guided, self-explanatory, live
The 3-step flow on screen1 · Pick a day — one-click examples (X8.7 storm day)2 · Watch the Sun — spikes = flares, colored bands = detections3 · Replay it live — the day streams at ×6000; every 🚨 toast is a real nowcast alertAlso on screen: merged-dataset card, filterable 2,891-flare catalog, “? how to read” panel, and a 📖 Guide & Glossary page explaining every keyword.
🔮 FUTURE WORK — MAJOR PROJECT
Forecast prototype (kept out of minor scope)• LightGBM P(flare ≤ 30 min), features from trailing windows• AUC 0.82 · 6/6 test flares alerted• median lead 192 s · p90 798 s at FAR = 2/daySame panel in the dashboard is explicitly labeled “future work” — scope discipline is part of the delivery.
Aditya-L1 Flare Watch · Minor Project · Solar-Flare Nowcasting
9

## Slide 10
SUMMARY
What stands delivered — and what comes next
Delivered (minor project)✅ 2,891-flare automated nowcast database (soft+hard)✅ 93.5% detection rate, validated vs NOAA GOES-16✅ Neupert-effect precursor measured: 117 s median✅ Merged dataset: 21.2M rows, single files per instrument✅ Dashboard + replay + in-app glossary — demo-ready✅ Reproducible: one-command rebuild, 6/6 tests
🔮 Next: Major project = forecasting
The prototype becomes the product:• attach LightGBM forecast + lead-time evaluation• exploit the 117 s hard-X precursor as a live feature• scale merged datasets as PRADAN releases more days“Nowcast today. Forecast tomorrow — on the same pipeline.”
Data: ISSDC PRADAN (SoLEXS + HEL1OS Level-1) · Reference: NOAA GOES-16 · Code: github.com/Peeyush1010/Minor-Project
Aditya-L1 Flare Watch · Minor Project · Solar-Flare Nowcasting
10